## Slide 1: CSE 350 Digital Electronics and Pulse Techniques
Mail: shomen.kundu@bracu.ac.bd
Desk: 4N166
Diode Logic
Course Instructor: Shomen Kundu (SDU)

## Slide 2: Abstract of Logic Gate:
This gates are abstract, because they just represent logical operations.

## Slide 3: Logic families

## Slide 4: Logic families
Digital Logic Families
Bipolar logic families
(electron and hole both are used as charge carrier)
Example: BJTs
Unipolar logic families
(Only one type of charge carrier dominates)
Example: MOSFET, JFET
i. PMOS logic families
ii. NMOS logic families
iii. CMOS logic families
Saturated
(saturation and Cutoff)
Unsaturated
(Active & Cutoff)

## Slide 5: Logic families
Saturated Logic Family: Uses Saturation & Cutoff region of a BJT for implementation of logic states.
  Resistor Transistor Logic (RTL)
  Diode Transistor Logic (DTL)
  Direct Coupled Transistor Logic (DCTL)
  Integrated Injection Logic (IIL)
  High Threshold Logic (HTL)
  Transistor-Transistor Logic (TTL)
Unsaturated Logic Family: Uses Active & Cutoff region of a BJT for implementation of logic states.
  Schottky TTL
  Emitter Coupled Logic (ECL)

## Slide 6: Logic families
Unipolar Logic Family: JFET, MOSFET etc. single charge carrier-based transistor logic families.
PMOS Logic Family
NMOS Logic Family
CMOS Logic Family

## Slide 7: Diode logic
OR gate and AND gate Design Techniques,
For each input we need a series resistance and a diode
Output will be connected with GND or VDD
For OR gate output will be connected to the GND via pull down resistance
For AND gate output will be connected to the VDD via pull up resistance.
Series resistance will be small.
Pull up / Pull down resistance will be large.

## Slide 8: Diode logic
OR Gate
Series and pull down
resistance can be chosen as

## Slide 9: Diode logic
Two input OR Gate
A | B | V1 | V2 | Vo | Y
0 | 0 | 0V | 0V |  | 
0 | 1 | 0V | 5V |  | 
1 | 0 | 5V | 0V |  | 
1 | 1 | 5V | 5V |  | 
Assume: Logic 1 means 5 V on input side. Logic 0 means 0 voltage/GND

## Slide 10: Diode logic
Case 1: A = 0, B = 0
First thing to check whether diodes are on or off.
FACT: We need at least 0.7 V to turn on any diode.
Conclusion: D1 and D2 are OFF.

## Slide 11: Diode logic
Case 2: A = 0, B = 1
First thing to check whether diodes are on or off.
# Here: D1 will be OFF and D2 will be ON

## Slide 12: Diode logic
Case 3: A = 1, B = 0 ( symmetrical to case 1 )
First thing to check whether diodes are on or off.
# Here: D1 will be ON and D2 will be OFF

## Slide 13: Diode logic
Case 4: A = 1, B = 1
First thing to check whether diodes are on or off.
# Here: D1 will be ON and D2 will be ON

## Slide 14: Diode logic
Two input OR Gate Findings
#4.28 V , 4.29 V
# logical High and Low can be
Different at input and output side
VOH = 4.28 V
( lowest of the outputs values
that can be considered as logic 1 )
A | B | V1 | V2 | Vo | Y
0 | 0 | 0V | 0V | 0 V | 0
0 | 1 | 0V | 5V | 4.2893V | 1
1 | 0 | 5V | 0V | 4.2893V | 1
1 | 1 | 5V | 5V | 4.2946 V | 1

## Slide 15: Power Dissipation Calculation
Theory:

## Slide 16: Max Power Dissipation
Example: Find the max power dissipation of the given circuit.

## Slide 17: Max Power Dissipation
Max power dissipation will be in the case 4
Or

## Slide 18: Diode logic
AND gate:

## Slide 19: Diode logic
Exercise: Analysis the four possible input and fill the table. Also find the VOL for this circuit.
A | B | V1 | V2 | Vo | Y
0 | 0 | 0V | 0V |  | 
0 | 1 | 0V | 5V |  | 
1 | 0 | 5V | 0V |  | 
1 | 1 | 5V | 5V |  | 
Hints: Logical low voltage at the output side -- Highest voltage for which the output is considered to be 0 or logic low.

## Slide 20: Diode logic
Try yourself,
1. Design a logic circuit, using diode logic.
2. For the given circuit find the maximum
power and average power.