## Slide 1: CSE 350 Digital Electronics and Pulse Techniques
Mail: shomen.kundu@bracu.ac.bd
Desk: 4N139
Analog to Digital Converter (ADC)
Course Instructor: Shomen Kundu (SDU)

## Slide 2: Op-Amp Review
Important terminals of Op-Amp
 Non-Inverting ( Positive ) input terminal
 Inverting ( Negative ) input terminal
 Higher power supply terminal
 Lower power supply terminal
 Output terminal

## Slide 3: Op-Amp Review
Operational Amplifier can be used for different configurations
Open Loop  Comparator, Used in ADC
Negative Feedback Amplifier, Used in DAC
Positive Feedback  Signal generator, Schmitt Trigger

## Slide 4: Op-Amp Review
For open loop configuration

## Slide 5: Analog to Digital Converter (ADC)
Signal can be classified into two broad categories.
Analog Signal ii. Digital Signal

## Slide 6: Analog to Digital Converter (ADC)
Physical world’s information are mostly analog. Analog means data could take
any real value at each instant of time.
In order to store/process we use digital data in our computers and microprocessor
Digital data means binary bit of strings.

## Slide 7: A/D conversion process

## Slide 8: Sampling
Sampling is the process of converting a continuous-time signal into a discrete-time signal by taking measurements at specific intervals in time.
A theorem,

## Slide 9: Quantization:
Quantization is a process by which we assign sampled and hold signal to some fixed preassigned values.
Midrise Quantization
Midtread Quantization

## Slide 10: Encoding
We can choose binary values for each of the level.
Assign lower Q level to 0
Then increase one for each next level

## Slide 11: Midrise Quantization:
Quantization Range | Quantization Level
( | 
( | 
( | 
( | 
( | 
( | 
( | 
( | 
Quantization Range | Quantization Level

## Slide 12: Mid tread Quantization ( Not symmetrical and Equally Spaced)
Quantization Range | Quantization Level
( | 
( | 
( | 
( | 
( | 
( | 
( | 
( | 
Quantization Range | Quantization Level

## Slide 13: Quantization Range, Level, code
Ex: Identify which one is Mid rise and Mid tread.

## Slide 14: Quantization Range, Level, code
Here,
As 4 V is a Quantization level. So, it is a mid tread quantization

## Slide 15: Quantization Range, Level, code
Ex: Identify which one is Mid rise and Mid tread.
Here,
As 5 V is not a Quantization level. So, it is a mid rise quantization

## Slide 16: Flash A/D converter
Features of the Flash A/D converter
This converter is very fast.
It requires one clock cycle to convert the analog to digital data.
It requires a lot components.

## Slide 17: Op-Amp
For open loop configuration

## Slide 18: Flash ADC design
Suppose you have a signal with and = 0V. Design a simple flash ADC converter.
Specifications:
3 bits output system
Equal quantization range and mid rise quantization
Active high Priority Encoder/ Active low Priority Encoder
[ Note: In Active high logic, logic 1 denotes high voltage and logic 0 denotes low voltage ( normal ),
In Active low logic, logic 1 denotes low voltage and logic 0 denotes high voltage]

## Slide 19: Flash ADC design
Design:
Here,
( One additional Comparator can also be used but it has no effect )

## Slide 20: Circuit
The following is the Circuit of a 3 bits Flash ADC,
For active high priority encoder, V+ of the comparator is connected to the input.

## Slide 21: Circuit Analysis
The following is the Circuit of a 3 bits Flash ADC,
Similarly,
You can find other voltage in this way.

## Slide 22: Circuit Analysis
Summary table:
Q Range | Q level | I7I6I5I4I3I2I1 | Binary (B2B1B0)
0 - 1.25 | 0.675 | 000 000 0 | 
1.25 - 2.5 | 1.875 | 000 000 1 | 
2.5 - 3.75 | 3.125 | 000 001 1 | 
3.75 – 5 | 4.375 | 000 011 1 | 
5 – 6.25 | 5.625 | 000 111 1 | 
6.25 – 7.5 | 6.875 | 001 111 1 | 
7.5 – 8.75 | 8.125 | 011 111 1 | 
8.75 - 10 | 9.375 | 111 111 1 | 

## Slide 23: Circuit Analysis
Encoder Truth Table:
( V+ of the comparator is connected to the Input )
Encoder can be implemented using
the combinational network.
I7I6I5I4I3I2I1 | Binary (B2B1B0)
000 000 0 | 000
000 000 1 | 001
000 001 1 | 010
000 011 1 | 011
000 111 1 | 100
001 111 1 | 101
011 111 1 | 110
111 111 1 | 111

## Slide 24: Circuit Analysis
Encoder Truth Table:
( For active low priority encoder V- of the comparator is connected to the Input )
Encoder can be implemented using
the combinational network.
I7I6I5I4I3I2I1 | Binary (B2B1B0)
111 111 1 | 000
111 111 0 | 001
111 110 0 | 010
111 100 0 | 011
111 000 0 | 100
110 000 0 | 101
1 000 000 | 110
000 000 0 | 111

## Slide 25: Quantization Error
Quantization Error = |Signal value – Quantized vale|
Max Quantization Error = ( = resolution )

## Slide 26: Problem:
Make a table with Quantization Range, Quantization Level and Binary values for the given ADC circuit.
What will be the final output if the input voltage
[ VREF = 12 V ]

## Slide 27: Dual Slope ADC
t<0, was connected to and was close.
t>0, will be connected to and will be open, Capacitor will start charging.
First slope depends on the input analog signal ( ) and it will integrate till ( Rising Time is fixed )
is the clock period and is clock frequency. Relation:

## Slide 28: Dual Slope ADC
After ,
will shift to
(Rising time )
( Falling time)

## Slide 29: Dual Slope ADC
After ,
will shift to
,

## Slide 30: Dual Slope ADC
Some important formula,
Rising time,
Falling time,
Decimal of digital output,
Reading time or conversion time,
Max reading time,
Max Sampling frequency,